## Slide 1: Wireless Metropolitan Area Network WMAN

## Slide 2: WMAN and Wireless Networks
WWAN
802.20 (proposed)
WMAN
70 Mbps
~50 Km
802.16a/e
WiMAX
New standard for
Fixed broadband
Wireless. Trying to do
for MAN what Wi-Fi
did for LAN.
WLAN
11-54 Mbps
~100m
802.11a/b/g
Wi-Fi®
Includes 802.11a/b/g.
Products must be
Approved for
Interoperability by the
Wi-Fi Alliance.
WiMAX: Worldwide Interoperability
for Microwave Access
Wi-Fi : Wireless Fidelity
WPAN
~1.5 Mbps
<10 m
802.15.1 (Bluetooth)

## Slide 3: Wireless Local Loop
Wired technologies responding to need for reliable, high-speed access by residential, business, and government subscribers ISDN, xDSL, cable modems
Increasing interest shown in competing wireless technologies for subscriber access
Wireless local loop (WLL)
  Narrowband – offers a replacement for existing telephony services
  Broadband – provides high-speed two-way voice and data service

## Slide 5: Advantages of WLL over Wired Approach
Cost – wireless systems are less expensive due to cost of cable installation that’s avoided
Installation time – WLL systems can be installed in a small fraction of the time required for a new wired system
Selective installation – radio units installed for subscribers who want service at a given time
  With a wired system, cable is laid out in anticipation of serving every subscriber in a given area

## Slide 6: WiMAX
WiMAX (Worldwide Interoperability for Microwave Access) (IEEE 802.16) technology offers:
  High speed of broadband service
  Wireless rather than wired access
  Broad coverage like cell phones
  WiMAX coverage; 50km (radius)
  WiMAX speed; 70 Mbps.

## Slide 7: WiMAX
WiMAX would operate similar to Wi-Fi but at a higher speeds, over greater distances, and for a greater number of users.
WiMAX system consists of two parts:
  WiMAX Tower; it is similar to cell phone tower with large coverage area (~8.000 square km).
  WiMAX Receiver ; it could be a small box or PCMCIA card.

## Slide 8: WiMAX
WiMAX has two modes:
  Non line-of-sight; where a small antenna on a computer connects to the WiMAX tower. It uses a lower frequency rang 2 GHz – 11GHz. (802.16a)
  Line-of-sight; where a fixed dish antenna points straight at the WiMAX tower. It uses higher frequency 10 GHz up to 66 GHz.

## Slide 9: WiMAX

## Slide 10: 802.16 Standards Development
Use wireless links with microwave
Use licensed spectrum
Are metropolitan in scale
Provide public network service to fee-paying customers
Use point-to-multipoint architecture with stationary rooftop or tower-mounted antennas

## Slide 11: 802.16 Standards Development
Provide efficient transport of heterogeneous traffic supporting quality of service (QoS)
Use wireless links with microwave or millimeter wave radios
Are capable of broadband transmissions (>2 Mbps)
Range - 30-mile (50-km) radius from base station
Speed - 70 megabits per second
Line-of-sight not needed between user and base station
Frequency bands - 2 to 11 GHz and 10 to 66 GHz (licensed and unlicensed bands)

## Slide 12: IEEE 802.16 Standards related to WiMAX

## Slide 13: WiMAX QoS
QoS means successful delivery of high value services such as voice and video.
QoS measured parameters are : Latency, Jitter and Packet Loss
Prioritizing Traffic is one solution to provide QOS for time sensitive traffic such as VoIP and video
Arrange the following applications into prioritizing categories:
  FTP - Streaming Audio and Video
  VoIP -Data Transfer, Web Browsing

## Slide 14: WiMAX Security
WiMAX systems were designed at the outset with robust security in mind. The standard includes state-of-the-art methods for ensuring user data privacy and preventing unauthorized access with additional protocol optimization for mobility.
Support For Privacy : User data is encrypted using cryptographic schemes. Both AES (Advanced Encryption Standard) and 3DES (Triple Data Encryption Standard) are supported with 128-bit or 256-bit key length

## Slide 15: WiMAX Security
Authentication :WiMAX terminal devices come with built-in digital certificates that contain their public key and MAC address. WiMAX operators can use the certificates for device authentication and use a username/password or smart card authentication on top of it for user authentication.
The Privacy and Key Management Protocol Version 2 (PKMv2) is used for securely transferring keying material from the base station to the mobile station, periodically re-authorizing and refreshing the keys.

## Slide 16: WiMAX Security
The integrity of over-the-air control messages is protected by using message digest schemes, such as AES-based Cipher-based message authentication codes “CMAC” or MD5-based HMAC.
To support fast handovers, WiMAX allows to use pre-authentication with a particular target BS to facilitate accelerated re-entry.